## Slide 1: Climate Adaptation Training 3.0: Extreme Heat + Flooding
This training is developed by the Urban Sustainability Directors Network (USDN) for use by member cities

## Slide 2: Purpose and Goals of Training
Develop better understanding of climate change vulnerability and risk assessments, adaptation planning and implementation
Integrate (or mainstream) climate change preparedness and resilience into planning activities
2
Notes: Speaker Notes:
The purpose of this training is to educate city staff about climate change and its impacts to city assets and operations. Climate change will affect many of the environmental conditions that our city currently considers during planning, design, construction, and maintenance of city assets and staff need to proactively address these challenges to maintain core city services and functions in a changing climate.
This training focuses on changes to riverine and coastal flooding, as well as number of extreme heat days, as a result of climate change and provides tools, exercises, and case studies to educate staff, encourage cross-department collaboration, and promote incorporation of climate change and resilience considerations into day to day activities. Many of the topics covered in this training are focused on flooding and heat hazards; however, the concepts can be applied to other climate change hazards as well. The goal of the training is to equip city staff with the knowledge and resources to “mainstream” or “operationalize” climate change preparedness and resilience into planning, engineering, operations, and maintenance activities.
Many cities are completing climate change vulnerability and risk assessments to better understand how climate change will impact their assets and operations. City staff are increasingly being asked to lead, manage, or participate in these assessments. This training also provides an overview of the climate change vulnerability and risk assessment process to build capacity for city staff to support these ongoing efforts and understand what type of data and other information may be requested of them as part of these assessments and why their participation is critical.

## Slide 3: Overview of Extremes: Heat & Floods
Notes: Speaker Notes:
Now we will discuss extreme heat and floods and how they are relevant to city assets and operations and provides an opportunity for the trainer to customize the content to reflect local climate projections.

## Slide 4: Changes in Extreme Heat
Images: Climate Central
4
Days above 90, 95, or 100 degrees are commonly used as a proxy measure of extreme heat, but extreme heat warnings are normally based on an index that combines heat and humidity to determine an extreme for a given location.
Extreme heat events have increased in frequency, severity and length, and this trend is projected to continue.
Notes: Speaker Notes:
Here we have the definition of extreme heat and information about observed and projected changes in extreme heat.
Image: http://www.climatecentral.org/gallery/maps/days-above-100f-projections

## Slide 5: Urban Heat Islands
5
Images: DC Policy Center, Bay Area Monitor
The Urban Heat Island (UHI) effect is a heat accumulation process caused by heat absorption and re-radiation of large impervious surface areas. Downtown building areas also reduce wind flow, trapping heat. This causes core urban areas with limited green space to be hotter than other areas.
Notes: Speaker Notes:
On a hot, sunny summer day, roof and pavement surface temperatures can be 50–90°F (27–50°C) hotter than the air, while shaded or moist surfaces—often in more rural surroundings—remain close to air temperatures. These surface urban heat islands, particularly during the summer, have multiple impacts and contribute to atmospheric urban heat islands. Air temperatures in cities, particularly after sunset, can be as much as 22°F (12°C) warmer than the air in neighboring, less developed regions. (EPA website)

## Slide 6: Extreme heat impacts
Buildings and Property: Stress on indoor climate control systems
Environmental: Habitat impacts; increased water demands; wildfires; invasive species
Health and Safety: Heat-related illness; respiratory illness; loss of power for light, pumping, communication, and air conditioning; water quality and quantity; vector-borne diseases; outdoor working conditions
Agricultural: Livestock fatalities or decreased production; Decreased crop yields
Supply chain: Disruption to transportation network (roads, rails, air)
Operations and finance: Heat damage to equipment; reduced capacity
6
Notes: Speaker Notes:
Extreme heat affects a range of disciplines from environmental to health and safety, posing challenges and impacts to supply chains, operation, and finance.
The Center for Disease Control report that extreme heat kills 600 Americans each year, more than any other weather phenomenon.
We will look at the impacts for our city in more detail in a moment as part of the adaptation planning process, which includes a task to review and understand the climate science for our region.

## Slide 7: Overview of Flooding Processes
Coastal
Riverine
Large waves, high tides, storm surge
Large river flow caused by heavy precipitation
Image: AP Photo/Michael Dwyer; Theodore Scontras/University of Maine
Image: NOAA NWS
A storm brings high winds resulting in storm surge and coastal flooding. Simultaneously, the same storm brings heavy precipitation, causing riverine flooding, which is exacerbated by high tides.
Coastal and Riverine
7
Notes: Speaker Notes:
Coastal Flooding: Caused by large waves, high tides and strong winds (hurricanes) elevating the coastal water level. Large waves can break over coastal barriers (pictured). Elevated coastal water levels can exceed the elevation of the beach and flood the developed area behind the beach
Riverine Flooding: Flow of river exceeds capacity of channel and water overflows channel banks. Large river flows caused by precipitation, melting snowpack, high runoff
Coastal Image Source:
http://www.livescience.com/11264-monster-waves.html
http://www.livescience.com/images/i/000/009/123/original/ig23_waves_coastal_flood_02.jpg?interpolation=lanczos-none&downsize=660:*
Credit: AP Photo/Michael Dwyer. Waves crash over the sea wall in Winthrop, Mass., Saturday, Jan. 4, 2003.
River image source:
http://www.weather.gov/dmx/preparefloodintro
http://www.weather.gov/images/dmx/Preparedness/River_Flood.jpg

## Slide 8: Changes in Extreme Precipitation
Source: National Climate Assessment, 2017
This is the number of 2-day precipitation events exceeding the threshold for a 5-year recurrence.
Defined as an event with more than 1, 2, or 4 inches of precipitation over a 24-hour period depending on geographic region.
Extreme precipitation events have increased in frequency and intensity and this trend is projected to continue.
8
Notes: Speaker Notes:
Here we have the definition of extreme precipitation and information about observed changes in extreme precipitation. This image represents the contiguous United States, but note that this may not represent all areas.
Image: https://science2017.globalchange.gov/chapter/7/
Image caption: Index of the number of 2-day precipitation events exceeding the station-specific threshold for a 5-year recurrence interval in the contiguous United States, expressed as a percentage difference from the 1901–1960 mean. The annual values are averaged over 5-year periods, with the pentad label indicating the ending year of the period. Annual time series of the number of events are first calculated at individual stations. Next, the grid box time series are calculated as the average of all stations in the grid box. Finally, a national time series is calculated as the average of the grid box time series. Data source: GHCN-Daily. (Figure source: CICS-NC and NOAA NCEI).

## Slide 9: Flooding Impacts
Buildings and Property: Water damage, reduced capacity
Environmental Flooding, erosion, habitat impacts
Health and Safety Loss of power for light, pumping, communication, air conditioning; water quality, vector-borne diseases
Supply chain Disruption to transport network
Operations and finance Water damage to equipment, reduced capacity
9
Notes: Speaker Notes:
Flooding impacts can be far reaching, and impact the same sectors that extreme heat also impacts. This slide provides a brief overview of some of the impacts that flooding causes.

## Slide 10: Useful Resources to Review for Local Climate Information
Resource | Data | Website
US Climate Resilience Toolkit’s Climate Explorer | Historical and projected county-level climate data | https://crt-climate-explorer.nemac.org/
National Climate Assessment | Historical and projected regional and sector-specific climate information and data | https://nca2014.globalchange.gov/
NOAA’s National Centers for Environmental Information (NCEI) | Comprehensive oceanic, atmospheric, and geophysical data | https://www.ncdc.noaa.gov/
NOAA’s NCEI State Climate Summaries | State-level information on historical and projected climate conditions | https://statesummaries.ncics.org/
NOAA Climate.gov | Climate maps and datasets that document various climate conditions | https://www.climate.gov/
You can also contact your regional and locally focused centers and state climatologists for more information and data: https://toolkit.climate.gov/help/partners
Notes: Speaker Notes:
Please update these resources as needed – current as of November 2018

## Slide 11: Climate Adaptation Planning Process & Game of Extremes Steps
Notes: Speaker Notes:
Now we will discuss the adaptation planning process and how it relates to the Game of Extremes.

## Slide 12: Process for Incorporating Climate Change into Project Planning
12
Notes: Speaker Notes:
This is a typical adaptation planning process followed by cities and other organizations. It has 7 main steps. Although cities should start at Step 1 (Review Science) in the cycle, many of the actions will be ongoing and/or will need to be revisited on a regular basis. These days, many cities are at Step 3 or 4 of the process and some may already have some asset or neighborhood-specific plans in place to tackle areas that are already at risk of extreme heat or flooding. Stakeholder engagement is at the center of the process, indicating the need to engage with communities, city staff, asset managers, resource agencies, and permitting agencies along the way. We will walk through each step of the process as part of this training, interspersed with game play.

## Slide 13: Process for Incorporating Climate Change into Project Planning: Game Steps
Asset Inventory
Vulnerability Assessment
Optional Risk Assessment
Adaptation Planning
Optional Implementation Exercise
13
Notes: Speaker Notes:
The Game of Extremes, which we’re about to play, focuses on a few of the steps in the process, namely, Asset Inventory, Vulnerability Assessment, an optional Risk Assessment, Adaptation Planning and Budgeting, and an optional Implementation exercise. The Climate Science step has been carried out for us as part of the game development, and you will receive a summary of the climate science analysis in the form of a scenario card in due course.

## Slide 14: Understanding your City
14
Understand who the key players are in an adaptation planning process.
Become familiar with the location of key assets and layout of the city.
Understand city demography.
Notes: Speaker Notes:
As noted for the previous slide, the first step in the adaptation planning process is normally a review of the science, but in the game, the science review has already been done and will be presented to players in the form of a climate scenario card. As such, we start the game with a focus on getting to know the city. In real life, this step is done by default through the knowledge and expertise of city staff, although the process of familiarizing oneself with key players in an adaptation planning process, and with the layout of your city from a risk and adaptation planning perspective are important steps in real-world adaptation planning.
The first step in the game will be to take some time to get acquainted with our fictitious city, our roles and the game board.

## Slide 15: Inventory Assets
15
Questions to consider during an Asset Inventory process:
What categories of assets should be considered (transportation, buildings, parks, etc.)?
Within each category, which assets are most critical for a well functioning city? How does the city define “critical”?
What data and information do we have relating to age, lifespan, condition, level of use of each asset?
What subset of critical assets will be carried forward to the vulnerability assessment?
 | Asset Inventory |  |  | 
 | Asset | Year Built | Condition (Poor, Moderate, Good) | Prior Damage History (Y/N)
Ex | Hospital | 1980 | Moderate | Y
1 | Burns Estates | 2005 | Good | N
2 | WWTP | 1950 | Moderate | Y
Notes: Speaker Notes:
The first section of the game will focus on inventorying the assets in the city and deciding which are the most critical for the city’s resilience. In a typical asset inventory process, we would identify categories and individual assets; meet with managers and stakeholders, collect data and identify gaps; and select the assets on which to focus further analysis. These steps are embedded in the questions listed on this slide.
The images to the right are of the game pieces and worksheets we’ll use during this step

## Slide 16: Assess Vulnerability
During this step, we ask ourselves:
Is the asset exposed to the climate stressor?
  For example, is the asset located in a heat island? Water Level Rise (WLR) flood zone? Riverine flood zone?
Is it sensitive to the climate stressor, e.g., would it be slightly or very impaired by extreme heat?
  Is the asset old and falling apart? Has it been impacted by a heat or flood event in the past?
How much adaptive capacity does the asset have, i.e., how easily can it be adjusted to deal with the stressor without being compromised.
  Would it be relatively easy or difficult to adapt the asset to the climate stressor?
16
Notes: Speaker Notes:
The Vulnerability Assessment process assesses the vulnerability of assets by thinking through the asset’s exposure, sensitivity, and adaptive capacity. This is an important process both in this game, but also in the real world. Understanding the vulnerability of your assets is an essential step to understanding how to protect them.
Elevated home image: https://www.wolfehousebuildingmovers.com/category/services/house-building-lifting/

## Slide 17: Assess Vulnerability
Groups use Asset Cards, Asset Inventory and Game Board to complete Vulnerability Assessment part of table.
Exposure
Sensitivity
Adaptive Capacity
Total Vulnerability Score
17
Example Definitions for “High” Exposure, Sensitivity, and Adaptive Capacity
Located in inner ring of heat island
Poor condition(or more than 30 years old); previously failed under heat conditions
Easily and cost effectively repaired, relocated or modified.
Vulnerability Assessment |  |  |  |  |  |  |  | 
WLR Exposure Score | Riverine Flood Exposure Score | Flood Sensitivity Score | Flood Adaptive Capacity Score | Heat Exposure Score | Heat Sensitivity Score | Heat Adaptive Capacity Score | Total Score (E+S+AC) | Ranking (1 to 10)
2 | 2 | 2 | 2 | 2 | 2 | 2 | 14 | 4
Groups use Total Vulnerability Score to prioritize adaptation strategy selection.
Notes: Speaker Notes:
During the Vulnerability Assessment section of the game, we will consider the exposure, sensitivity and adaptive capacity of each of our prioritized assets from the asset inventory. One of the steps in this process will be to decide how we will define high, medium and low exposure, sensitivity and adaptive capacity. The definitions at the bottom of this slide are possible definitions for high exposure, sensitivity and adaptive capacity.
In order to come up with a vulnerability score for each asset (and thereby compare one asset vulnerability to another), we add up its individual exposure, sensitivity and adaptive capacity scores. In real life, one of these scores, e.g., sensitivity, may be weighted more than another one, e.g., adaptive capacity.

## Slide 18: Assess Consequence of Impact
18
 | Consequence Assessment | 
 | Potential Consequence of Flooding | Potential Consequence of Extreme Heat
Senior Center | Closure of facility; Evacuation of vulnerable population; Perpetuation of mold problems and associated illness. | Power outage causing closure of facility; Lack of air conditioning with vulnerable population
Main Roadway | Impassible roadways; Damage and destruction of roadway infrastructure; Inhibiting emergency and evacuation travel; | Damage and destruction of roadway infrastructure; Inhibiting emergency and evacuation travel;
Focus on most vulnerable and critical assets for consequence evaluation.
Consequence ranges from negligible to catastrophic, depending on how badly the impact would affect an asset and the people who depend on it.
Notes: Speaker Notes:
A risk assessment helps differentiate the severity of impacts to different assets that may be exposed to the same climate hazard. In this section of the game, we will develop qualitative consequence statements describing the consequence of an extreme heat impact on an asset. Groups identify consequence of the heat impact on each asset in terms of relative damage, disruption, and cost and complete Risk Assessment Table

## Slide 19: Plan Adaptation
Typical steps for strategy selection:
Prioritize adaptation needs based on vulnerability, timing of impact, criticality
Identify strategies based on asset characteristics and climate hazard
Evaluate strategies based on feasibility, cost, co-benefits, social equity and other factors
Strategies can be:
Structural
Governance
Asset-specific
Regional
19
Notes: Speaker Notes:
Physical or structural adaptation strategies refer to on-the-ground changes to infrastructure and, for extreme heat, are most likely focused on redesigning or protecting the asset (or population) from heat.
Governance strategies (such policies, programs etc) include building code and policy updates, disaster response plans, cool roof or impervious surface ordinances, or city-wide adopting of green infrastructure design guidance which can improve community resilience to future climate change hazards incrementally over time as new projects are implemented
In addition to differences between structural and non-structural adaptation measures, adaptation strategies can either be asset-specific or regional in nature. Regional strategies will require collaboration across multiple stakeholders and agencies and may be necessary particularly at political boundaries (for example, county or city lines) where an integrated solution is required.
In this section of the game,
Review potential adaptation options and associated costs.
Teams will strategize how to protect assets with allotted funding.
Teams should record results in their own workbook in the short- and long-term adaptation plan tables

## Slide 20: Implement Adaptation Measures
Questions to consider when implementing an adaptation measure:
Which city agencies would lead the effort to implement the strategy? Who else needs to be engaged?
What are the main barriers to implementing the strategy?
What are the key opportunities for integrating climate adaptation considerations into standard city decision-making processes?
20
Notes: Speaker Notes:
Implementing adaptation measures requires careful attention to ensuring political will, funding and support within the city exist to enable the successful implementation of an action. In this section of the game, we will choose one of the adaptation strategies from the previous section and use it to think through key implementation questions.
Tree planting: https://caseytrees.org/event/volunteer-johnson-middle-school-community-tree-planting/
Rail painted white image: https://www.telegraph.co.uk/news/uknews/road-and-rail-transport/10204211/Heat-hits-train-punctuality-tracks-to-be-painted-white-to-counteract-hot-weather.html